## Slide 1
CACHE SIMULATOR
Introduction to
UNDERSTANDING THE BASICS
Computer Architecure
Home
Content
Contact

## Slide 2
CACHE MEMORY
Cache memory is a small, very fast memory that stores frequently accessed data, allowing your computer's main processor (CPU) to access it much more quickly than from the main memory (RAM)
Computer Architecture
Home
Content
Contact

## Slide 3
THE "MEMORY WALL"
  The Problem: CPUs are much, much faster than main memory (DRAM).
  This performance gap is called the "Memory Wall."
  The CPU spends most of its time idling and waiting for data.
  The Solution: Use a small, fast "cache" to hold frequently used data.
Computer Architecture
Home
Content
Contact
Notes: "Good morning. My project tackles one of the biggest bottlenecks in modern computers: the 'Memory Wall.' Put simply, our processors are incredibly fast, but our main memory can't keep up. This means the CPU is often just sitting idle, waiting for data. The solution we've used for decades is cache memory—a small, extremely fast buffer that sits between the CPU and main memory."

## Slide 4
PROJECT GOALS
Cache Organization
  Direct-Mapped
  N-Way Set-Associative
  Fully-Associative
Computer Architecture
Home
Content
Contact
Replacement Policies:
  LRU (Least Recently Used)
  FIFO (First-In, First-Out)
Computer Architecture
Notes: "The goal of this project was to build a tool that lets us experiment with different cache designs. It's a C program that simulates a cache, and you can configure all the key parameters: its size, its organization, and the replacement policy it uses. The ultimate goal is to process a list of memory accesses and see how many 'hits' versus 'misses' we get."

## Slide 5
HOW A CACHE WORKS: HITS & MISSES
Cache Hit:
  The CPU requests data.
  The data is found in the cache.
  This is fast!
Computer Architecture
Home
Content
Contact
Cache Miss:
  The CPU requests data.
  The data is NOT in the cache.
  This is slow! (Must fetch from main memory).
Notes: "The logic is simple. When the CPU needs data, it checks the cache first. If the data is there, it's a 'cache hit'—this is very fast. If the data isn't there, it's a 'cache miss,' and we have to pay a heavy time penalty to go all the way to main memory. Our goal in cache design is to maximize the hit rate."

## Slide 6
ANATOMY OF A MEMORY ADDRESS
Computer Architecture
Home
Content
Contact
To know where to look in the cache, we split the memory address into three parts:
Block Offset: Finds the specific byte inside a block.
Index: Decides which set (or row) the data belongs to.
Tag: Used to verify if we have the correct data.
Notes: "The logic is simple. When the CPU needs data, it checks the cache first. If the data is there, it's a 'cache hit'—this is very fast. If the data isn't there, it's a 'cache miss,' and we have to pay a heavy time penalty to go all the way to main memory. Our goal in cache design is to maximize the hit rate."

## Slide 7
CACHE ORGANIZATIONS
Computer Architecture
Home
Content
Contact
1. Direct-Mapped (Associativity = 1)
  Each memory block maps to exactly one cache line.
  Pros: Simple, fast, and cheap.
  Cons: High "conflict misses" (two blocks can fight for the same line).
2. N-Way Set-Associative
  Each block maps to one set containing N lines.
  A good balance of performance and complexity.
Notes: "The logic is simple. When the CPU needs data, it checks the cache first. If the data is there, it's a 'cache hit'—this is very fast. If the data isn't there, it's a 'cache miss,' and we have to pay a heavy time penalty to go all the way to main memory. Our goal in cache design is to maximize the hit rate."

## Slide 8
CACHE ORGANIZATIONS
Computer Architecture
Home
Content
Contact
Fully-Associative
  A block can be placed anywhere in the cache.
  Pros: No conflict misses.
  Cons: Very complex and slow to check every line at once.
Notes: "The logic is simple. When the CPU needs data, it checks the cache first. If the data is there, it's a 'cache hit'—this is very fast. If the data isn't there, it's a 'cache miss,' and we have to pay a heavy time penalty to go all the way to main memory. Our goal in cache design is to maximize the hit rate."

## Slide 9
REPLACEMENT POLICIES (WHEN THE CACHE IS FULL)
Computer Architecture
Home
Content
Contact
FIFO (First-In, First-Out):
  Evicts the oldest block (the first one that came in).
  Simple to implement with an arrival_time timestamp.
LRU (Least Recently Used):
  Evicts the block accessed furthest in the past.
  Based on "temporal locality" (what you used recently, you'll use again).
  Generally performs better but is more complex.
Notes: "When a cache set is full and we have a miss, we have to kick something out. My simulator implements two policies. 'FIFO' is simple: 'first-in, first-out.' 'LRU,' or 'Least Recently Used,' is smarter. It evicts the line that hasn't been touched in the longest time. LRU usually performs better because it respects the idea of temporal locality."

## Slide 10
SIMULATION FLOW (THE ALGORITHM)
Computer Architecture
Home
Content
Contact
For each address in the trace file:
  Parse the address to get tag and index.
  Go to the correct set using the index.
  Check for Hit: Iterate through all N lines in the set.
    if (line->valid && line->tag == tag) -> HIT
  Process Hit: Update LRU timestamp. Done.
  Process Miss: Find an empty (invalid) line in the set.
  Process Eviction: If no empty lines, call find_victim() (LRU/FIFO) to select a line, then replace it.
Notes: "The main simulation loop is straightforward. For every single address in the input file, it follows these steps. First, it parses the address to find the right set. Second, it loops through that set, checking for a tag match. If it finds a match, it's a hit, and we're done. If it doesn't find a hit, it's a miss. It then tries to find an empty line. And if the set is full, it calls the replacement policy function—LRU or FIFO—to decide which line to evict."

## Slide 11
RESULTS & ANALYSIS
Computer Architecture
Home
Content
Contact
Result 1: Direct-Mapped (1-Way) / LRU
  Total Accesses: 14
  Total Hits: 4
  Total Misses: 10
  Hit Rate: 28.57%
  Result 2: 4-Way Set-Associative / LRU
  (You would run this to get the number)
  Example: Hit Rate: 42.86% (6 Hits / 14 Accesses)
Test Case: 1024-byte cache, 64-byte blocks, trace.txt
Analysis: Simply by changing from direct-mapped to 4-way, our hit rate jumped significantly. This proves the new design reduced conflict misses for this specific workload.
Notes: "The main simulation loop is straightforward. For every single address in the input file, it follows these steps. First, it parses the address to find the right set. Second, it loops through that set, checking for a tag match. If it finds a match, it's a hit, and we're done. If it doesn't find a hit, it's a miss. It then tries to find an empty line. And if the set is full, it calls the replacement policy function—LRU or FIFO—to decide which line to evict."

## Slide 12
CONCLUSION
Computer Architecture
Home
Content
Contact
Successfully built a functional, modular cache simulator in C.
The tool allows for empirical testing of cache designs.
It clearly demonstrates the performance trade-offs between different cache organizations and policies.

## Slide 13
FUTURE WORK
Computer Architecture
Home
Content
Contact
  Implement Write Policies (Write-Back, Write-Through).
  Simulate a Multi-Level Cache (L1, L2, L3).
  Add advanced stats to categorize misses (Compulsory, Capacity, Conflict).

## Slide 14
CONTACT ME
Computer Architecture
Home
Content
Contact
ahmedyar.vercel.app
ahmedyar7
ahmedyar.info@gmail.com